Instruction Manual

For

38" x 54" AMERICAN  100 TON

Cutting & Creasing Press

From

General Offices:

THOMSON NATIONAL PRESS COMPANY

115 Dean Avenue

Franklin, MA 02038

Phone: (508) 528-2000

Fax: (508) 520-7129

E-mail: thomsongroup@thethomsongroup.com

Web page:  www.thethomsongroup.com

NOTICE

The American National Standards Institute has adopted a new set of safety standards for all hand fed platen presses.  We strongly urge that press users comply with these new standards.  To obtain a copy of ANSI B65.5-1996, please contact:

NPES

1899 Preston White Drive

Reston, VA 22091-4367

703/264-7200-phone

703/620-0994-fax

Once you have reviewed these standards, we urge you to contact us if you need any further assistance.

FOREWORD

This Instruction Manual has been prepared to give you helpful information on the installation, operation, care and maintenance of Thomson National Cutting and Creasing Presses, so that you may operate them at maximum efficiency and with a minimum of maintenance.



Your Thomson National Cutting and Creasing Press is skillfully designed and expertly constructed of high-grade materials, and will easily meet all the service demands of normal use.



To insure the successful operation of the machine, it must be operated within its load limitations, using proper dies and makeready procedure.  The machine should be kept well lubricated, reasonably clean, and free from foreign matter.



Operators are urged to read this manual thoroughly before operating the machine.  Throughout the manual, warnings are included as part of service and operating procedures.  Warning signs are also placed on the machine to remind operators of hazards resulting from improper procedures.  The purpose is to prevent accidents and establish safe operating practices.

TABLE OF CONTENTS

SECTION - I

GENERAL DESCRIPTION

PAGE

Main parts	6

Distinguishing Operating Features	6

SECTION - II

INSTALLATION

Selecting Location	7

Leveling and Placement of Air Loc Pads	7

Cleaning Parts	8

Removing Parallel Bar	8

Wiring	9

Lubrication	9

Starting Up a New Machine	9

Gears - New Machine	9

Oil	10

Meter Units	10

Electric Motor or Variable Speed Drive	10

Connecting Rod Bushings & Impression

Sleeve Bearings	10

Gears - Normal Operation	11

Air Line Lubricator	11

Flywheel Bearings	11

Pillow Blocks	11

Inspection and Servicing	12

Bypass Procedure ……………………………………………………... 13

SECTION - III

OPERATION

Press Cycle - Start/Stop	13

Impression Adjustments - Dual Micrometer Design	13

Impression Adjustment Increments	16

Mounting Dies in Press	17

Die Mounting	17

Centering Die	17

Die Loads and Press Capacity	18

Die Loads	18

Press Loads	18

Safe Platen Press Operation	19

The User's Responsibility	19

Guarding the Point of Operation	19

Safety Devices	19

Management Safety Tips	20

Press Operator's Safety Tips	20

Safety Test Trip	22

SECTION - IV

CARE, MAINTENANCE, & OPERATIONAL DIFFICULTIES

General Care	23

Air Line Filter	23

Air Line Lubricator	23

Resetting Bridge Face Parallel with Frame Face	23

Clutch/Brake Description ……………………………………………… 27

Changing the Clutch or Brake Plates	28

Assembling and Disassembling Clutch/Brake	28

Clutch/Brake Lining Thickness ………………………………………. 29

SECTION - V

TROUBLE SHOOTING

Bridge Stuck On Center	30

Causes of Bridge Cam Failure	30

Causes of Bridge Lugs Slipping	30

Bridge Face Not Parallel With Frame Face,

Resulting Problems	31

Makeready Problems	31

Problems with the Press (Inconsistent Cutting)	32

Interrupted Machine Cycles	33

Electrical System Failure	33

Spare Parts ……………………………………………………………... 34

SECTION I

GENERAL DESCRIPTION

The Thomson Cutting and Creasing Press is a hand-fed Platen Press designed for use with steel rule dies for the manufacture of paper, corrugated and fiber boxes, display cutouts, paper toys, gaskets, greeting cards, automobile door and body panels, decals, nameplates, faceplates, membrane switches, spacers and many other products of the paper and plastic industries.

These machines are also used with electric die heaters for roll leafing, embossing, thermal die cutting and hot die cutting.

The words PLATEN or BRIDGE as used in this manual are synonymous and refer to the same part.

The Thomson line of machines is constructed with a fabricated steel bridge and frame and dual micrometer impression control.  It is air clutch operated, with a live flywheel, and is designed for continuous operation, manual start with automatic stop, automatic start and stop with adjustable dwell in the open position, and dwell in closed position as an option.  This machine is crank action in design.

MAIN PARTS

The main parts of the machine are the frame, bridge, connecting rods, flywheel, pinion shaft, main shaft, and gear wheels.

DISTINGUISHING OPERATING FEATURES

The bridge makes a direct, square, and theoretically perfect impact upon the die, rolling to the frame face, free and unrestrained with perfect parallelism.

Adjustable bridge lugs are provided for setting the face of the bridge parallel with the face of the frame.

The face of the frame is inclined from the vertical, eliminating the need for frisket fingers, as the processed sheet lies naturally against the bridge on this inclined angle.

All dies must be properly located so that the press load is balanced relative to the connecting rod pull.  If this is impossible, then bearers must be used to balance the load and prevent tipping of the bridge, causing slippage of the bridge lugs.  (See Makeready Instruction Manual.)

A hard steel cutting plate should always be used on the press.  Use of a "soft" cutting surface will increase the press load and reduce die life.  Proper makeready procedures will result in cutting operations which allow cutting without the necessity of the die contacting the cutting plate.

SECTION II

INSTALLATION

The complete machine comes with rust preventative on exposed surfaces to protect it from corrosion and bolted to heavy skids to protect it from damage.

SELECTING LOCATION

Leave the press on skids until it is moved into its permanent position.  See the floor plan for the area required and distribution of weight.  A solid foundation is recommended for the machine.  It should be located over the building beam supports if possible.  Proper consideration of working space around the installation area and good lighting for the operator are important factors in selecting a location.

WARNING:  Check the capacity of the lifting equipment in your plant before moving your new press.

LEVELING AND PLACEMENT OF AIR LOC PADS

Place the oil drip tray on the floor, remove the skids, and place the vibration pads under the feet of the press.  Thicker pads go down first, then the thinner pads.  Place a machine level on the main shaft or on the pinion shaft, and drive wedges under the frame corners until a level position is obtained.  Shims should be placed between thick and thin vibration pads.  Remove the wedges and secure the press to the floor.  See figure 2-1.

CLEANING PARTS

Uncrate all parts and clean thoroughly to remove all dirt, foreign matter and protective coatings.  Check all parts of the machine to see that they are free from foreign matter that may be lodged in holes, pockets, or gear teeth.

Check and clean all oil holes to make sure they are not obstructed with dirt, grease or paint.

REMOVING PARALLEL BAR

1.  Attach airline to press (80-PSI RCFM required).  A 1" NPT quick disconnect is located on the left hand side of the Press, close to the floor

2.  Wire main power lines from disconnect switch to Press.  (See wiring diagram supplied.)  Check rotation of flywheel.

Note: Do not attempt to cycle the press under power until the parallel bar is removed.

3.  On the control panel, place the RUN/BYPASS selector switch in the BYPASS position.  Press the START button to engage the clutch.  Keep the button depressed while turning the flywheel.  (Releasing the start button will disengage the clutch, and engage the brake.)

4.  To remove parallel bar, turn flywheel the opposite direction of arrow indicated on flywheel until bridge opens.

4-A.  See BYPASS PROCEDURE, page 13.

5.  Remove the parallel bar.

6.  Pre-lubricate the press before start-up (see lubrication section, starting new machine)

7.  Visually inspect the machine for any debris or obstructions.

8.  The press is now ready to run.

CAUTION:

TURN THE PRESS OVER VERY SLOWLY WITH THE FLYWHEEL RUNNING IN THE PROPER DIRECTION TO MAKE SURE EVERYTHING FUNCTIONS WELL BEFORE APPLYING FULL POWER.  THE MAIN GEARS SHOULD REVOLVE AWAY FROM OPERATOR IN THE DIRECTION AS INDICATED BY THE ARROW ON THE SIDE OF THE GEARS.

WIRING

The machine is equipped with a master control console and panel box completely wired at the factory.

Only qualified personnel should install and service electrical equipment.

WARNING:  Only connect incoming electrical power as indicated on the enclosed wiring diagram.

A separate, fused, wall disconnect switch should be installed for each machine.

LUBRICATION

WARNING:  Turn off main electrical power and stop flywheel before applying any lubrication.

Starting Up a New Machine

Fill oil reservoir.  To fill lines and lubricate bearings before starting new machine, pull instant feed knob on Bijur Lubricator and release to allow pump to discharge.  Repeat until oil is in evidence at all bearings.

Gears - New Machine

Important:  Before starting up a new machine, make sure all teeth are well lubricated.  Lubricate manually if necessary.  Never operate the machine with the gears dry.

Make sure that oil holes are free of dirt, paint, or any other foreign matter.

Thomson Cutting and Creasing Presses have bearings that work under relatively slow speeds and extreme pressures.  Proper lubrication affects the life of a press, and is one of the most important factors influencing its proper operation and long life.  Better results will be obtained by applying a small quantity of lubricant frequently, rather than a large supply at long intervals.  Recommended lubricants are shown on metal plates or decals attached to each machine.

All areas of the machine that require oil lubrication are taken care of automatically by the bijur lubricating system consisting of a pump unit which forces oil through a branched tubing line to Meter-Units, one of these being located at or near each bearing.  The pump measures the total quantity of oil fed to the system and the Meter-Units proportion this quantity according to the individual requirements of the bearings.  (See data sheet for pump unit.)

Oil

Use only a clean mineral oil of SAE 30 viscosity.  NEVER use "dripless" oil or oil containing graphite, soap, or other foreign substances.  Refill reservoir before oil level drops to the bottom of oil level gauge.

Meter Units

Meter-Units are self-contained, non-adjustable units.  Letters stamped on them indicate the type and the flow rate- the higher the number, the greater the flow.  The Meter-Units offer such high resistance to oil flow that they are the controlling factors in oil distribution.  As a result, there is practically no variation in oil delivery, normally caused by flow resistance in the tubing, variation in bearing wear, or initial fit.  Check valves in the Meter-Units prevent reverse flow and keep the tubing full of oil at all times.  A Meter-Unit may be mounted directly at a bearing, at an adjacent junction or at a tee head.

Use FJB Meter-Units with this pump.

Electric Motor or Variable Speed Drive

All lubricating points must be checked and lubricated in accordance with manufacturer's recommendations furnished with motor or drive.

Connecting Rod Bushings & Impression Sleeve Bearings

These bearings are lubricated by hand.  Alemite fittings should be fed grease four times for an eight-hour shift.

Gears - Normal Operation

Lube lines are fed by the automatic lubricating system.  Maintain oil level in oiling system and check occasionally for oil film on gear teeth.

Air Line Lubricator

Keep filled with SAE 10 Oil.  The purpose of this lubricator is to protect the walls and packings in the air system from rusting and drying out.

Flywheel Bearings

The flywheel bearings are pre-greased, sealed bearings.

Pillow Blocks

Once every six months apply one half ounce of high quality lithium base grease to the pillow block for the flywheel shaft and the pinion shaft.

CAUTION:

AN 	EXCESS QUANTITY OF GREASE WILL CAUSE BEARINGS TO RUN WARM AND WILL DAMAGE THE BEARING SEALS.

INSPECTION AND SERVICING

With the pump feeding the system, inspect for oil at the bearings: also, check that there are no leaks at the tubes or connections.

IF SOME BEARINGS ARE GETTING INSUFFICIENT OIL, INSPECT FOR:

1.  Low oil level in reservoir

2.  Broken or cracked tubes or loose connections.  Wipe off tubes and connections, and watch for leaks.  When replacing a tube, see that it is properly clipped to prevent vibration.

3.  Flattened lubricator pump outlet tube.

4.  Clogged lubricator pump filter.  Remove filter disk and replace with a new one.  Check every six months.

5.  Dirt in Reservoir.

IF ONLY ONE BEARING IS GETTING INSUFFICIENT OIL, INSPECT FOR:

1.  Flattened oil tube of loose connection to the meter-unit feeding this bearing.

2.  Slow feeding Meter-Unit.  Make sure oil reaches inlet of Meter-Unit when pump is feeding; also, check rate of feed with Meter-Unit connected so as to drip free.  Should there be any questions as to the rate, compare it with a Meter-Unit of the same rate number on another part of the machine.  If Meter-Unit is feeding a proper quantity in accordance with its rate number, and an increased feed is desired, use same type and next higher number.  The Meter-Units are replaced complete with head.  Never disassemble a Meter-Unit or drill it out, as this will ruin its operation.  Do not try to test a Meter-Unit by blowing through them.  REMEMBER oil flows through Meter-Units very slowly, and IN ONE DIRECTION ONLY, as indicated by the arrow plainly stamped on each Meter-Unit.

SECTION III

OPERATION

BYPASS PROCEDURE

1.  Have power to main panel "on," but all other functions should be "off."  Make sure the "safe/ready/run" button is pulled out, in the "run" position.

2.  Make sure the flywheel is not in motion.

3.  Press "run/bypass" switch on the main control panel to "bypass" position.  (See figure 2-2, Control Panel.)

4.  Press cycle "start" button.  The clutch will engage.

5.  Release cycle "start" button.  The clutch will disengage, and the brake will engage.

6.  Return the "run/bypass" switch to "run" position for normal press operation

PRESS CYCLE - START /STOP

-Turn power on

-Put main motor into operation, and select desired speed (note: main motor will not run unless air pressure is on)

-Press should be in "run" mode

-Select desired cycle:

•	Single cycle allows one press cycle only (generally used for setting up)

•	Auto cycle activates "dwell open" timer, allowing the press to stop in the opened position for the amount of time set on timer

•	Continuous allows press to run continuously

•	Dwell closed activates dwell-closed timer, which allows the press to stop in the closed position for the amount of time set on the timer

-Pull Stop/Safe ready button out, placing it in the "ready position"

-Auxiliary safety must be placed forward in the "run" position

-Press cycle "START"

-To stop machine, depress "STOP/SAFE READY" button

IMPRESSION ADJUSTMENTS - DUAL MICROMETER DESIGN

The impression is adjusted using the dual micrometers.  Each side of the bridge is adjusted separately.  This allows for faster and more accurate makeready, reducing down time to a minimum.

First loosen the impression sleeve locking bolts using the supplied wrench.  With an open-ended wrench, turn the impression sleeve to the desired setting and then re-tighten the lock bolts.  (See figures next page)

WARNING:  Never advance one side of the bridge ahead of the other more than 0.015", or 1/64".

DO NOT PACK UNDER THE CUTTING PLATE IN PREFERENCE TO ADVANCING IMPRESSION BY MICROMETER ADJUSTMENTS.

CAUTION

NEVER TAKE AN IMPRESSION WITHOUT FIRST TIGHTENING THE LOCKING BOLTS ON IMPRESSION SLEEVE.

ALWAYS RETURN IMPRESSION ADJUSTMENT TO "0" WHEN STARTING A NEW JOB.

Impression Adjustment Increments, Thomson American

FIGURE INDICATES APPROXIMATE INCREMENTS BETWEEN EACH INDICATOR MARKING (in inches).

LINE            IN              OUT

(.9375) 0       .000            .000

1                  .009            .009

2                  .009            .009

3                  .009            .009

4                  .010            .009

5                  .010            .005

6                  .011            .005

7                  .011            .005

8                  .012            .005

9                  .012            .005

10                .012            .005

11                .012            .004

12                .012            .004

13                .013            .003

14                .012

15                .012

16                .011

17                .011

18                .011

19                .010

20                .010

21                .009

22                .009

23                .008

24                .007

25                .006

26                .005

27                .004

28                .003

29                .002

30                .002

31                .001

MOUNTING DIES IN PRESS

Die Mounting

CAUTION: Before mounting die on press, refer to the safety standard for stand-alone presses, ANSI #B65.5-1996, section 18.2, Inch-safe-service method.

For your safety and for ease of operation, chaseless die mounting fasteners have been supplied with your press.  Refer to the makeready manual for proper die setup procedures.

Centering Die

It is very important to have the center of force of the die located in line with the centerline of connecting rod pull to prevent unnecessary tipping of bridge and movement of the bridge lugs.  To help center dies in the press, a die mounting template has been supplied with the press.

CAUTION: Before mounting dies, turn off motor and return wrap around safety device to its back or "safe" position.

If it is necessary to have an unbalanced load, bearers should be inserted for balance.  When using bearers, note that bearers increase the load on the press, while decreasing the available cutting load.

DIE LOADS AND PRESS CAPACITY

Years of research and testing have been performed by Thomson National Engineers on forces required to die cut or emboss all types of sample material.

The maximum tonnage recommended by various manufactures of cutting and creasing presses can become confusing when a comparison of machines is made unless the basis used by each company is defined and understood.

Die Loads

Cutting and Creasing loads can be determined by testing a sample using a specially constructed laboratory press.  This test takes into consideration material grain, die construction, and stripping material load.  The results can be converted to the maximum die size allowable to stay within recommended die cutting load ratings.

Press Loads

The total load on a press is usually much greater than the theoretical die cutting load and is made up of the following:

1.  Loads created by die imperfections such as:

A. Dull cutting rule

B. Cutting rule of unequal height.

C.  Poor die design, specifying cutting rule of incorrect height, bevel, or thickness, or incorrect height of creasing rule, lumber, or stripping material.

2.  Load created by poor makeready that is soft or excessive.

3.  Load created by material variations caused by changes in moisture content, grain density, or thickness.

4.  Excess load created by careless impression micrometer settings.

5.  Load created by worn machine components and the natural deflection of highly stressed parts.

6.  Load created during cutting and creasing of material.  This is the diecutting load used as a basis for Thomson recommendations.

The total press load will vary with the above conditions and can be up to 3 times the recommended die-cutting load.  A Thomson press with a die load recommendation of 100 tons could be equivalent to another manufacturer's press load recommendation of 300 tons.

SAFE PLATEN PRESS OPERATION

The User's Responsibility

This section of the Instruction Manual is not intended as a Safety Code.  Its purpose is to alert persons associated with platen presses to the importance of establishing safe operating and maintenance procedures.

Throughout this manual warnings have been inserted calling attention to safe practices and procedures.  Day to day safety is a vital part of everyone's job.  A press accident can result in loss of production, damage to the press, personal injury and breakdown of shop morale.

Make every effort to keep your presses safe for production.  A daily press inspection, over and above normal maintenance, of all guarding and safety devices and brakes is a good way to start.

Guarding the Point of Operation

The "point of operation" is the area created when the platen reaches a position of parallelism with the die face just before contact between the die and material to be converted.  The use of proper "point of operation" devices coupled with a well-trained operator is the best insurance against mishaps.

It is the responsibility of the employer to provide and insure the use of properly applied and adjusted devices on every operation performed on a platen press consistent with the dies being used, with the feeding methods being used, or other features unique to operation, so as to provide maximum protection to the operator.

Safety Devices

The following safety devices are provided with your press, and are the minimum required for proper operation.  Other devices may be required if the press is used for a purpose other than that for which it was originally intended.

1.  WRAP AROUND SAFETY DEVICE

This device stops normal stroking of the press if the operator's hands are placed in the point of operation as the platen closes.  The die should not be removed except when this device is placed in its back safety position, causing the platen to become inoperative.  The "SAFE-STOP/READY" push-button must also be depressed.

2.  PLATEN SAFETY DEVICE

Stops normal cycling of the press, when activated by the operator.

WARNING:  This Auxiliary Safety Device & Platen Safety Device must be set and maintained according to the requirements of ANSI B65.5-1996.

Management Safety Tips

1.  Make certain that the press operators are trained and instructed in safe methods of operation and provide adequate supervision to enforce safe operating procedures.

2.  Set up a program of press inspection as required by ANSI 65.5-1996.

3.  Establish a preventative maintenance program.

4.  Make frequent evaluation checks of all press safety devices during actual production runs.  Correct any unsafe conditions before resuming operation.

5.  Provide a clean, safe, uncluttered area around each press.

6.  Stop the press immediately when a malfunction is reported and correct before resuming operation.

7.  Establish, publish and enforce a firm policy of safety regulations.

8.  Take immediate action to prevent a recurrence of all "close calls" before they become accidents.

9.  Never change wiring.

10.  Never change air piping.

11.  Never substitute component parts.

12.  Dies and stripping material should be checked and maintained for proper cutting and stock ejection.

13.  Never run a press that has been modified.

14.  Only use the press for its intended purpose.

Press Operator's Safety Tips

1.  Never operate this machine with any press or safety device malfunction.

2.  Perform daily inspections as required by ANSI B65.5-1996 Section 16.3.1 (Refer to Safety Test Trip, and see figure 3.4)

3.  Make a pre-operation check of all operating controls, safeguarding devices, bottom and side sheet or material guides, alert signals, die and material being worked.

4.  Never attempt to correct or remove misfed sheets before stopping the platen in the fully open position.  Report die trouble to supervisor.

5.  Never operate, service or adjust the press, or install dies without proper understanding of the instructions in the Instruction Manual.

6.  Never sit on, stand on or bend over the platen with the flywheel turning.

7.  Never makeready or set stock guides before stopping the drive motor.

8.  Obey alert or warning signals on the press.

9.  Stop the machine if it malfunctions.  Report any questionable operation, unusual action, unsafe condition or improper maintenance to the proper person.

10.  When changing the setting of press controls for a different mode of operation, test the machine cycle to be sure it operates as expected.

11.  Check the work area to be sure it is free of objects that could cause one to slip or trip.

12.  Wear proper personal protective equipment specified by the employer.

13.  Shut off power to the press when it is not in use.

14.  Never talk to another person while feeding the press.

15.  Never reach over, under or around press safety devices or try to bend, check, modify or remove point of operation safety devices.

16.  Develop a sense of personal safety awareness.  Observe all safety regulations.  Be on the lookout for hazardous conditions and discuss control of them with your supervisor.

17.  Always follow all operating procedures outlined in ANSI B65.5-1996

Safety Test Trip

The auxiliary safety test trip is a device to measure the acceptable distance between the platen and the die-mounting surface after the wrap around safety device is actuated.  When the platen is cycled, the test trip contacts the top surface of the platen, causing the tripped wrap around safety device to stop the press.  To run the test, the press should be operating at its highest speed, to ensure that the requirement for the minimum remaining distance is met at all operating speeds.  After the platen strikes the test trip, the remaining distance should be no less than 100mm between the platen and the die mounting surface.  The 1996 safety standard states that operators MUST run this test before regular operation every day to guarantee the proper working condition of the safety device and braking system.  Return the safety test trip to back position after successful completion of the test for normal operation of the machine.  Below is a diagram of the proper test procedure.

SECTION IV

CARE & MAINTENANCE

GENERAL CARE

In order to get the most efficiency from your Thomson Cutting and Creasing Press, it should be given the good care due any precision machine.  It should be kept reasonably clean and free from foreign matter.  Do not allow waste material to collect in bridge cam well, on rocker seats, or in gear teeth.

While the press is ruggedly built of high quality materials and relatively trouble free, you should carefully follow all operating instructions, and check the machine for proper adjustments and wear at the first indication of improper performance.

Keep the machine properly lubricated at all times and do not abuse it by overloading, either with too heavy a job, poor makeready, dull dies, or variations in material conditions such as thickness, moisture content, and grain.

Air Line Filter

Drain water and residue whenever shown in the reservoir if not equipped with an automatic trap.

Air Line Lubricator

Keep filled with SAE 10 Oil.  The purpose of this lubrication is to protect the walls and O-rings and gaskets in the air system from rusting and drying out.

RESETTING BRIDGE FACE PARALLEL WITH FRAME FACE

PROCEDURE FOR SQUARING BRIDGE & ADJUSTING BRIDGE CAM ROLLER ON THOMSON 38 x 54 AMERICAN PRESS

Please be sure that the main motor is turned off and the flywheel motion has stopped before proceeding.  Remove the die and all makeready from the press.

1.  Place the parallel bar (shipped with the press) into the machine, hanging it from the top of the platen by the pin sticking out from the edge of the bar near the top.  Be sure to place the bar an equal distance from each side of the platen.

2.  Adjust the impression to lightly squeeze the bar in the press.  Be sure that both sides are adjusted such that the indicators read exactly the same.  The platen should not be tipped from side to side.

3.  Place the press in the by-pass position (see by-pass instructions page 13) and turn the flywheel by hand in the direction of the arrow until the squaring bar is very close to contacting the frame face or heater face (about .030").  Release cycle "start" button.

4.  Loosen both the top and bottom bridge lugs.

5.  With the press in the by-pass position, rotate the flywheel until the bar is squeezed firmly in the press.  Release the clutch and engage the brake.

6.  Adjust the bridge lugs so that they are firmly against the bridge guide (both top and bottom) and tighten securely.

See figure 4-1.

7.  Check to be sure that the cam rollers turn freely in this position.  If not, adjust the cam rollers using the eccentrics on either end of the roller shafts such that the rollers turn freely.  See figure 4-1.

8.  Back off the flywheel until the top lug is on the guide block about 3/16" and make sure that the center line of the rollers are into working portion of the cam way.  The rollers should turn freely in this position; otherwise, adjust eccentrics.  (See figure 4-2A)

9.  With the press in the by-pass position, back off the flywheel until the platen is about one-quarter open.  Release the bypass switch.

10.  Remove the parallel bar.

11. Using a .002" feeler gauge check for clearance between each side of the rollers and the cam ways.  The .002" feeler should slide completely through from side to side without obstruction on one side of the cam way.  On the opposite side you should be unable to start the feeler gauge in any position.  This test is performed to assure that the cam rollers are parallel to the cam ways and do not make contact with the front of the cam ways on one end of the roller and the rear of the cam way the other end of the roller.  (See figure 4-2b)

12. Return impression adjustments to zero settings on each side and mount your die.  Be sure the die is mounted such that the load is centered in the press.  Unbalanced loads will accelerate press wear and necessitate repeating the squaring procedure often.

CAUTION

IF THE BRIDGE CAM ROLLER STANDS MOVE FROM THEIR SELECTED SETTING, WEAR AND CAM BREAKAGE MAY RESULT.  CHECK SCREWS PERIODICALLY.

# CLUTCH/BRAKE DESCRIPTION

The clutch/brake unit consists of three components:

- The clutch plate (E) carrying the friction pads, fastened to the flywheel and fixed in the rotary direction but allowing the pads or plates to float axially.

- The brake plate (F) carrying the friction pads, fastened to the machine frame and fixed in the rotary direction but allowing the pads or plates to float axially.

- The clutch/brake body, fixed to the shaft and controlled by an external power source.

This assembly consists of three parts: The clutch cover (1), the brake cover (2) fastened by bolts and fixed firmly to the machine shaft, and the piston (4) with two friction faces (D) and piston seals (8) & (9).

# OPERATION

In the spring engaged position, the coil springs (7) exert a force on the piston (4) causing it to travel to the left (brake side) as shown in drawing and engaging friction face (D) with brake plate (F) creating a stopping and holding action.

When compressed air is introduced into chamber (C) the air pressure overcomes spring force and causes the piston (4) to travel to the right (clutch side) as shown in drawing engaging the clutch plate (E) attached to a rotating flywheel.

CHANGING THE CLUTCH PLATES OR THE BRAKE PLATES

If the clutch or the brake plate has to be replaced, power to the machine must be locked out.  With the air off the unit will be in the spring applied, brake on position, making the clutch plates accessible for removal.

If the replacement of the brake plates is required, unbolt the hex head bolts holding the plate halves to the machine frame or the reaction pin lugs.  Apply compressed air to the piston assembly shifting it to the clutch on position.  The brake plates are now accessible for removal and replacement.  After the brake plates have been replaced, exhaust the air, returning the unit to the spring applied position.

ASSEMBLY AND DISASSEMBLY OF THE CLUTCH/BRAKE

Periodically, the clutch/brake unit must be taken off the shaft on which it is mounted.  For this purpose the unit is equipped with two threaded extraction holes on the clutch cover.  To remove from the brake side, remove two hub socket head cap screws, diametrically opposed, and use their threaded holes as extraction holes.

The clutch cover and the brake cover are fastened by socket head cap screws.  The two halves are under tension caused by the compression of the brake springs.  To avoid injury it is important to use the following procedure for disassembly.

1.  Loosen and remove two diametrically opposed socket head cap screws.

2.  Replace with two extended length cap screws and threaded nuts.  Thread the cap screw until it has bottomed out and adjust the nut until it rests on the brake cover.

3.  Progressively loosen the two nuts and the remaining socket head cap screws allowing the covers to separate under control and relax the spring compression.

4.  Remove the cap screws when they are totally loosened.  Continue to progressively loosen the nuts on the extended cap screws until the springs are completely relaxed.  It is then safe to remove the brake cover.

5.  Before removing the piston, match mark the piston with a match mark on the circumference of the clutch cover to ensure assembly integrity in the exact position of disassembly.  Piston seals should always be replaced when the piston is removed to avoid accidental damage to the seal.

6.  To assemble the unit, reverse the disassembly steps.  All socket head cap screws should be tightened to the torque values shown below.  Apply Loctite to all cap screw threads before tightening.

TIGHTENING TORQUE VALUES FOR SCREWS AND NUTS

SCREWS 8.8 	M6	M8	M10	M12	M14	M16	M18	M20	M24

TORQUE		10	25	49	86	135	210	290	410	710

MAINTENANCE AND SAFETY INSTRUCTIONS

In most cases, the clutch/brake is considered a safety component of the machine.  Therefore, correct operation is very important and maintenance instructions must be followed.

1.  Periodically check the wear of the friction linings.  Lining thickness for the 38x54 press should never be less than 10 mm thick.  Only use plates and linings supplied by the manufacturer.  The co-efficient of friction and the material will vary from manufacturer to manufacturer and could affect the clutch and brake torque.

2.  The clutch/brake must have a major inspection and overhaul every three million cycles or every three years.  Inspection and repair should be done by a qualified Goizper repair shop or factory agent.  The unit must be disassembled and the following parts inspected and replaced where necessary.

a) Friction plates and hinges

b) Brake springs

c) Inner and outer piston seals

d) fasteners, washers and bushings

Lubrication of piston seals should be done with heat resistant grease.  All fasteners use lockwashers.  Threads should be treated with Loctite 271 before tightening.

SECTION V

TROUBLE SHOOTING

BRIDGE STUCK ON CENTER

Recommended procedure for moving the bridge from dead center:

A.  Turn off the main motor, and wait until the flywheel comes to a complete stop.

B.  Place the press into the by-pass position (see page 9, items 4 and 4-A)

C.  Insert A 1" diameter rod into one of the holes on the circumference of the flywheel, and turn the flywheel in the direction opposite of the arrow.

D.  Once the press opens, remove any obstructions, and inspect the makeready and the press for damage.

E.  Return the press to "run" condition.

CAUSES OF BRIDGE CAM FAILURE

1.  Worn bridge cam and bridge cam roller

2.  Bridge cam roller shaft out of adjustment

3.  Bridge face not parallel with frame face, causing it to rise on impression.

4.  Bridge lugs adjusted improperly, causing straining action with motion of bridge cam.

5.  Machine operating backwards.

6.  Machine operating at excessive speeds.

7.  Bridge Cam Roller Stand Bolts loose.

8.  Worn rockers on the bridge.

CAUSES OF BRIDGE LUGS SLIPPING

1.  Dies mounted off center or unbalanced load.

2.  Cutting rule in die is dull.

3.  Extra stock fed into, or fell into press.

4.  Parts of die, such as rule or quoins, fall into the press.

5.  Tools left on steel cutting plate.

6.  Lug bolts loose.

7.  Bridge Cam Roller out of adjustment.

BRIDGE FACE NOT PARALLEL WITH FRAME FACE - RESULTING PROBLEMS

1.  Bridge lifts on impression

2.  Cutting rules are abused and become dull.

3.  Uneven cut top to bottom.

4.  Overload of press.

5.  Unnecessary makeready

6.  Steel cutting plate is cut into and damaged.

7.  Slippage of bridge lugs.

8.  Bridge Cam failure

9.  Unsatisfactory die cutting.

MAKEREADY PROBLEMS

If the makeready is soft the job will fade away and will also tend to dull the cutting rule more than necessary.

Never use more than .003 gummed paper for spotting up.  Gummed paper .006" thick will bear the form off and cause overloading of the press.

Never use any kind of tape other than make-ready tape.

If a soft steel plate or brass plate is substituted for the hard cutting plate, it is very likely that the machine will be overloaded, causing a main shaft, bridge shaft, crank pin, or connecting rods to break.

Fibber boards that have been bonded together with silica, and also metal lined boards that have uneven perforations and are used for blow out proof gaskets, cause considerable trouble in fading out of work.

Plastics of varying density may cause inconsistent cutting.

Variation in moisture content of board and change in direction of grain will affect die-cutting results.

Consult make-ready manual for proper make-ready instructions

PROBLEMS WITH THE PRESS (INCONSISTENT CUTTING)

A.  Crank pins loosened or bent.

B.  Worn main shaft bushings.

C.  Worn connecting rod bushings.

D.  Worn or stretched connecting rod.

E.  Insufficient impression to take up machine clearance.

F.  Bridge lugs slipped.

G.  Impression sleeves badly worn.

H.  Fatiguing of parts.

I.   Bridge cam improperly adjusted.

INTERRUPTED MACHINE CYCLES

A.  Auxiliary wrap-around safety device Micro-Switches are set too critically and are actuated by vibration.  WARNING:  Micro-Switch must be set for less than 1/2" movement of auxiliary safety device to stop press.

B.  Platen Safety Trip Device should have at least 1/16" Gap between actuating plunger and microswitch.

C.  Air Pressure Drops - Loss of Air (Pressure below 50 PSI will cause the press to stop)

(1) If the drop in air pressure occurs only when the start button is pressed, check for leaks in the clutch or for an inadequate supply.

(2) Check the Roto Seal for any air leakage.

(3) Check for loose connections or broken or kinked hose.

(4) Check all air valves.

Electrical System Failure

1.  Check all connections in panel box and floor console for loose wires, which may cause faulty operation of relays.

2.  All relays should be firmly seated in their sockets

3.  Check fuses

4.  Check for broken wires

NDEX

Air Line Filter	23

Bridge Cam Failures	30

Bridge Cam Well	31

Bridge Face (NOT PARALLEL)	31

Bridge Lugs	30

Interrupted Cycles	33

Bridge Stuck On Center	30

Cleaning Parts	8

Connecting Rod Bushings	10

Die Load	18

Die Mounting	17

Electrical System Failure	33

Flywheel Bearings	11

General Care	23

Guarding Point of Operation	19

Impression Adjustment	16

Impression Sleeve Bearings	10

Leveling the Press	7

Load Recommendation	18

Lubrication	9

Main Parts	6

INDEX (continued)

Management Safety Tips	20

New Machine	9

Operators Safety Tips	20

Parallel Bar Removal	8

Pillow Block	11

Placing Die in Press	17

Platen Press Safety	19

Press Capacity	18

Press Loads	18

Press Operation	13

Resetting Bridge Parallel with Frame Face	23

Selecting Location	7

Shutting Down Machine	9

Starting Up New Machine	9

User's Responsibility	19

Vibration Pads	7

Wiring	9